Experiment 2: Construction designs

1. Experiment with one basic design of tubes (50mm, no paint or holes) compared to weather station data

Sunny day	Station / n = 6	Regular tubes / n = 12
Mean temperature	23.83	24.31 / + 0.48
Maximum temperature	27.73	31.12 / + 3.39
Minimum temperature	21.05	20.71 / - 0.33
Standard deviation	0.1333	0.3519
Mean / humidity	87.01	86.25 / - 0.76
Maximum humidity	96.38	98.75 / + 2.38
Minimum humidity	71.14	64.17 / - 6.97
Standard deviation	1.6868	1.7675

2 days of measurements (2 min intervals) of which data are interpolated using linear interpolation. 6 PVC constructions have been used without aeration. 2 sensors have been placed in a coffee-cup (with holes at the bottom) in each PVC tube.

2. Experiment with 5 different (50mm) tube designs (2 each with 2 sensors) compared to weather station data

Sunny Day	Station / n = 10	Regular tubes / n = 4	Holes only / n = 4	Reflective tape / n = 4	Insulating foil no holes / n = 4	Insulating foil / with holes / n = 4
Mean temperature	23.96	24.80 / + 0.83	24.51 / + 0.54	24.86 / + 0.89	24.73 / + 0.76	24.89 / + 0.93
Maximum temperature	28.83	33.20 / + 4.37	32.33 / + 3.50	33.61 / + 4.78	31.54 / + 2.71	33.24 / + 4.41
Minimum temperature	19.68	19.14 / - 0.55	19.23 / -0.46	19.20 / - 0.48	19.48 / - 0.20	19.41 / - 0.27
Standard deviation	0.0378	0.266	0.231	0.393	0.244	0.259
Mean / humidity	85.43	82.64 / - 2.79	83.54 / - 1.89	82.48 / - 2.94	83.15 / - 2.27	81.69 / - 3.74
Maximum humidity	97.34	100.40 / + 3.06	100.73 / + 3.39	99.99 / + 2.65	102.29 / + 4.95	99.62 / + 2.28
Minimum humidity	67.15	50.46 / - 16.69	53.50 / - 13.65	46.80 / - 20.35	52.98 / - 14.16	50.58 / - 16.57
Standard humidity	1.2937	1.0161	1.0683	1.6263	2.6022	1.1095

 1 day of measurements with 30 sensors (10 in station, 20 divided over 10 PVC pipes), 1440 observations per sensor (1min).
The PVC pipes in this experiment had a diameter of 50mm and the sensor was placed on a plastic mesh above the surface.
3. Experiment with 5 different (50mm) tube designs (2 each with 2 sensors) compared to weather station data

Rainy day	Station / n = 10	Regular tubes / n = 4	Holes only / n = 4	Reflective tape / n = 4	Insulating foil no holes / n = 4	Insulating foil / with holes / n = 4
Mean temperature	21.92	21.78 / - 0.14	21.64 / - 0.27	21.77 / - 0.15	21.92 / - 0.00	21.76 / - 0.15
Maximum temperature	25.96	30.00 / + 4.03	28.89 / + 2.93	28.79 / + 2.83	29.20 / + 3.24	27.62 / + 1.66
Minimum temperature	20.56	20.31 / - 0.25	20.33 / - 0.23	20.33 / - 5.63	20.33 / - 0.23	20.23 / - 0.33
Standard deviation	0.0487	0.1062	0.2403	0.1920	0.0706	0.1269
Mean / humidity	92.17	95.56 / + 3.39	98.62 / + 6.44	96.09 / + 3.92	93.89 / + 1.71	95.94 / + 3.77
Maximum humidity	97.10	100.97 / + 3.87	103.87 / + 6.77	100.90 / + 3.80	99.43 / + 2.32	104.00 / + 6.90
Minimum humidity	78.88	65.62 / - 13.26	68.80 / - 10.07	81.06 / + 2.18	66.50 / - 12.37	70.13 / - 8.74
Standard humidity	0.7788	0.9851	3.1028	1.3478	1.7420	2.4877

 1 day of measurements with 30 sensors (10 in station, 20 divided over 10 PVC pipes), 1440 observations per sensor (1min).
The PVC pipes in this experiment had a diameter of 50mm and the sensor was placed within the horizontal part of the tube.

3. Experiment with 5 different (50mm) tube designs (2 each with 2 sensors) compared to weather station data

Rainy day	Station / n = 6	Regular tubes / n = 3	Holes only / n = 3	Insulating foil no holes / n = 4	Insulating foil with holes / n = 4
Mean temperature	21.40	21.29 / - 0.12	21.24 / - 0.16	21.31 / - 0.09	21.30 / - 0.10
Maximum temperature	22.53	22.70 / + 0.13	22.59 / + 0.06	22.89 / + 0.37	22.62 / + 0.10
Minimum temperature	20.68	20.55 / - 0.14	20.52 / - 0.16	20.55 / - 0.14	20.56 / - 0.13
Standard deviation	0.0443	0.0500	0.0250	0.0866	0.0380
Mean / humidity	96.65	99.73 / + 3.08	99.83 / + 3.18	101.48 / + 4.83	99.92 / + 3.27
Maximum humidity	99.93	102.16 / + 2.23	103.04 / + 3.11	105.82 / + 5.89	102.60 / + 2.67
Minimum humidity	92.78	96.52 / + 3.74	96.31 / + 3.53	96.27 / + 3.49	95.90 / + 3.12
Standard humidity	0.7060	0.5204	0.5551	1.6407	0.5249

 1 day of measurements with 18 sensors (6 in station, 12 divided over 12 PVC pipes), 1440 observations per sensor (1min).
The PVC pipes in this experiment had a diameter of 25mm and the sensor was placed within the horizontal part of the tube.
The day has been relatively cold and rainy with a small temperature range throughout the day (no sunshine at any time).