EXPERIMENT 1: DIFFERENT BUTTON- & TEMPORAL RESOLUTION

Due to the limited storage capacity that most micro-sensors have, which means a trade-off between sensor resolution and temporal resolution (assuming the monitored period will remained the same). At high resolution of both relative humidity and temperature on the iButton Hydrochron (DS-1923), 2048 measurements will be possible, the temporal resolutions for different time-spans can be seen in table 1. The data used consists of 2016 measurement at 5 minute intervals, which are either scaled-up to 10080 measurements at 1 minute intervals or scaled-down to 168 hourly observations (30 sensors are used).

Table 1: Possible time covered using different sensor resolutions

Interval	Low res (4096 readings)	High res (2048 readings)
1 minute	2 days 20 hours	1 day 10 hours
10 minutes	4 weeks	2 weeks
30 minutes	12 weeks	6 weeks
1 hour	24 weeks	12 weeks
2 hour	48 weeks	24 weeks
6 hours	2 years 42 weeks	1 year 21 weeks
12 hours	5 years 32 weeks	2 years 42 weeks
1 day	11 years 12 weeks	5 years 32 weeks

As most growing seasons are > 12 weeks, 1 hour intervals at high resolution will not be a viable option with these sensors. This experiment has tested two groups of sensors (high and low interval, n in both groups = 15) with measurements during one week at 5 min intervals. The 5 min interval has been scaled-up to 1 min intervals using NA.Spline and NA.Approx, whereas the 5 min interval is also scaled-down to 1 hour intervals using the same techniques. Differences between these temporal and sensor resolutions can be seen in table 1a and 1b. Due to the large number of measurements, there are only small differences between the two different interpolation techniques, with NA.Spline generally resulting in slightly higher maximum and lower minimum values. The means remains the same in most cases. The relative humidity slightly surpasses 100% for the different sensor resolutions (minute-data) in most cases, and the maximum difference is 1.2%. The largest difference for temperature is just over 0.5°C. When looking at the extremes, the temperature for low-res sensors – using NA.Approx is above 30°C for 2 hours (163 minutes), while this is only 2 minutes for high-res sensors. When using NA.Spline, 2 hours are measured above the 30°C threshold (169 minutes); for the high-res sensors this is still only 8 minutes. Humidity is never above 100% for more than 6 minutes (high-res sensor using NA.Spline). When using 5-min intervals, little information is lost when using 1 hour intervals in stead of 1 min intervals. Most differences are caused by sensor resolution (up to 0.53°C and 0.47% RH), compared to 0.16°C and 1% RH difference between minute & hour intervals based on 5 min intervals during 1 week.
1A: Na.approx (no changes is maximum and minimum value)

	Low res / temperature (minutes)	High res temperature (minutes)	Low res temperature (hours)	High res temperature (hours)	Low res / humidity (minutes)	High res humidity (minutes)	Low res humidity (hours)	High res humidity (hours)
Maximum	30.12	30.02	30.10	29.86	99.94	100.23	99.61	99.06
Difference	0.73	0.51	1.28	0.39	10.13	6.69	12.42	10.04
Std. Dev.	0.40	0.24	0.35	0.13	3.12	3.81	3.06	3.29
Mean	22.37	22.35	22.37	22.36	90.45	90.93	90.43	90.92
Difference	0.34	0.08	0.86	0.16	2.48	1.86	4.20	3.84
Std. Dev.	0.26	0.05	0.26	0.04	1.13	1.20	1.16	1.19
Minimum	18.11	18.54	18.11	18.59	64.33	63.86	64.80	64.50
Difference	0.10	0.03	0.51	0.09	0.47	0.55	1.65	1.44
Std. Dev.	0.17	0.02	0.17	0.03	0.36	0.36	0.49	0.44

1B: Na.spline (values might be calculated outside measured limits)

	Low res / temperature (minutes)	High res temperature (minutes)	Low res temperature (hours)	High res temperature (hours)	Low res / humidity (minutes)	High res humidity (minutes)	Low res humidity (hours)	High res humidity (hours)
Maximum	30.22	30.04	30.14	29.88	100.05	100.23	99.68	99.23
Difference	1.53	0.79	1.29	0.42	13.15	11.15	12.57	10.07
Std. Dev.	0.38	0.23	0.35	0.13	3.20	3.85	3.10	3.29
Mean	22.37	22.35	22.37	22.36	90.45	90.93	90.44	90.93
Difference	0.86	0.16	0.87	0.16	4.18	3.96	4.27	3.93
Std. Dev.	0.26	0.05	0.27	0.05	1.16	1.22	1.18	1.21
Minimum	18.01	18.54	18.11	18.59	64.15	63.69	64.82	64.56
Difference	0.49	0.08	0.56	0.09	1.21	1.20	1.80	1.41
Std. Dev.	0.16	0.02	0.18	0.03	0.36	0.36	0.51	0.46

22.35497
> max(temp.t1)
[1] 30.10669
> max(temp.t2)
[1] 29.35665
> max(temp.h1)
Error: object 'temp.h1' not found
> max(humd.t1)
[1] 98.73892