Difference between the individual sensors in (1) tubes*; and (2) the weather station. A total of 6 sensors have been placed in a weather station and 12 sensors have been divided over 6 different tubes. Aeration in the PVC tubes (sensor placed at 1.5m) has been limited, with only aeration near the sensor – which has been insufficient to provide air circulation in the construction. Measurements have been done during two days (noon from 28-30 June 2014), which have included rain, but also a lot of sunshine. The data in the table is derived from measurements at 2 min intervals, which have been interpolated to data at 1 minute intervals by using NA.Spline in R. The mean temperature is slightly higher in the pipes (< 2%), while the relative humidity is less than 1% higher in the station than in the PVC tues. Difference in extremes are much higher (see figure 1), with a 15% higher maximum for temperature (> 4° C), and > 2% higher relative humidity. The mean temperature does not differ a lot between the station and tubes (± 2%), but the relative humidity is > 14% lower in the PVC tubes – which is a similar difference as can be seen for the temperature. Extremes are found between 12 and 3 pm.

	Station (°C) / NA spline	Station (°C) / NA approx	Pipes (°C) / NA spline	Pipes (°C) / NA approx	Station (% RH) / NA spline	Station (% RH) NA approx	Pipes (% RH) / NA spline	Pipes (% RH) NA approx
Maximum / measurement	28.76		33.05		97.36		99.93
Max difference	0.42		5.64		9.35		22.01
Max st. deviation	0.17		1.83		3.39		6.16
Mean / measurement	23.38		23.81		88.30		87.86
Mean difference	0.15		0.06		4.76		4.26
Mean st. deviation	0.06		0.20		1.75		1.28
Minimum / measurement	20.93		20.49		66.83		52.66
Min difference	0.02		0.63		0.77		0.91
Min st. deviation	0.01		0.02		0.31		0.28

* The PVC tubes have a 50mm diameter and the sensor is placed at 1.50 m inside a paper cup with holes. No other aeration has been used in this experiment. The PVC tubes have a white color, but no additional reflective paint has been applied.